## Slide 1: Chapter 10: Application Layer
Curriculum Title
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 10: Application Layer

## Slide 2: Chapter 10 - Sections & Objectives
10.1 Application Layer Protocols
  Explain the operation of the application layer in providing support to end-user applications.
    Explain how the functions of the application layer, session layer, and presentation layer work together to provide network services to end user applications
    Explain how common application layer protocols interact with end user applications.
10.2 Well-Known Application Protocols and Services
  Explain how well-known TCP/IP application layer protocols operate.
    Explain how web and email protocols operate.
    Explain how DNS and DHCP operate.
    Explain how file transfer protocols operate.
Notes: 2
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 10: Application Layer

## Slide 3: 10.1 Application Layer Protocols
Notes: 10 – Application Layer
10.1 Application Layer Protocols

## Slide 4: Application, Presentation, and Sessio Application Layer
Application Layer:
  Closest to the end user.
  Used to exchange data between programs running on the source and destination hosts.
Notes: 10.1 – Application Layer Protocols
10.1.1 – Application, Presentation, and Session
10.1.1.1– Application Layer

## Slide 5: Application, Presentation, and Session Presentation and Session Layer
Presentation Layer function:
  Formatting data at the source device into a compatible form for the receiving device.
  Compressing data.
  Encrypting data.
Session Layer Function
  Create and maintain dialogs between source and destination applications.
Notes: 10.1 – Application Layer Protocols
10.1.1 – Application, Presentation, and Session
10.1.1.2– Presentation and Session Layer

## Slide 6: Application, Presentation, and Session TCP/IP Application Layer Protocols
  Domain Name Server (DNS) TCP,UDP 53 - Translates domain names, such as cisco.com, into IP addresses.
  (BOOTP) – Bootstrap Protocol - BOOTP is being superseded by DHCP.
  Dynamic Host Configuration Protocol (DHCP) UDP client 68, server 67 – Dynamically assigns IP addresses to client stations at start-up.
  Simple Mail Transport Protocol (SMTP) TCP 25 - Enables clients to send email to a mail server.
Post Office Protocol (POP) TCP 110 - Enables clients to retrieve email from a mail server.
Internet Message Access Protocol (IMAP) TCP 143 - Enables clients to retrieve email from a mail server, maintains email on server.
File Transfer Protocol (FTP) TCP 20 and 21 - Reliable, connection-oriented, and acknowledged file delivery protocol.
Trivial File Transfer Protocol (TFTP) UDP 69 – simple connectionless file transfer protocol.
Hypertext Transfer Protocol (HTTP) TCP 80, 8080 - Set of rules for exchanging text, graphic images, etc. on the World Wide Web.
Hypertext Transfer Protocol Secure (HTTPS) TCP, UDP 443 – Uses encryption and authentication to secure communication.
Notes: 10.1 – Application Layer Protocols
10.1.1 – Application, Presentation, and Session
10.1.1.3– TCP/IP Application Layer Protocols

## Slide 7: How Application Protocols Interact with End-User Applications Client-Server Model
Client and server processes are considered to be in the application layer.
Application layer protocols describe the format of the requests and responses between clients and servers.
Example of a client-server network is using an ISP’s email service to send, receive and store email.
Notes: 10.1 – Application Layer Protocols
10.1.2 – How Application Protocols Interact with End-User Applications
10.1.2.1– Client-Server Model

## Slide 8: How Application Protocols Interact with End-User Applications Peer-to-Peer Networks
Data is accessed from a peer device without the use of a dedicated server.
Each device (known as a peer) can function as both a server and a client.
Notes: 10.1 – Application Layer Protocols
10.1.2 – How Application Protocols Interact with End-User Applications
10.1.2.2– Peer-to-Peer Networks

## Slide 9: How Application Protocols Interact with End-User Applications Peer-to-Peer Applications
A P2P application allows a device to act as both a client and a server within the same communication.
P2P applications require that each end device provide a user interface and run a background service.
Notes: 10.1 – Application Layer Protocols
10.1.2 – How Application Protocols Interact with End-User Applications
10.1.2.3 – Peer-to-Peer Applications

## Slide 10: How Application Protocols Interact with End-User Applications Common P2P Applications
Common P2P networks include:
  G2
  Bitcoin
  BitTorrent
  eDonkey
Some P2P applications are based on the Gnutella protocol, where each user shares whole files with other users.
Many P2P applications allow users to share pieces of many files with each other at the same time –this is BitTorrent technology.
Notes: 10.1 – Application Layer Protocols
10.1.2 – How Application Protocols Interact with End-User Applications
10.1.2.4 – Common P2P Applications

## Slide 11: How Application Protocols Interact with End-User Applications Researching Peer-to-Peer File Sharing
Notes: 10.1 – Application Layer Protocols
10.1.2 – How Application Protocols Interact with End-User Applications
10.1.2.5 – Lab – Researching Peer-to-Peer File Sharing

## Slide 12: 10.2 Well-Known Application Layer Protocols and Services
Notes: 10 – Application Layer
10.2 Well-Known Application Layer Protocols and Services

## Slide 13: Web and Email Protocols Hypertext Transfer Protocol and Hypertext Markup Language
When a web address or uniform resource locator (URL) is typed into a web browser, the web browser establishes a connection to the web service running on the server, using the HTTP protocol.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols
10.2.1.1 – Hypertext Transfer Protocol and Hypertext Markup Language

## Slide 14: Web and Email Protocols HTTP and HTTPS
HTTP is a request/response protocol.
Three common HTTP message types are:
  GET - A client request for data.
  POST - Uploads data files to the web server.
  PUT - Uploads resources or content to the web server.
HTTP Secure (HTTPS) protocol uses encryption and authentication to secure data.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols
10.2.1.2 – HTTP and HTTPS

## Slide 15: Web and Email Protocols Email Protocols
Email clients communicate with mail servers to send and receive email.
Mail servers communicate with other mail servers to transport messages from one domain to another.
Three protocols for email:
  Simple Mail Transfer Protocol (SMTP) to send email.
  Post Office Protocol (POP) to retrieve email.
  Internet Message Access Protocol (IMAP) to retrieve email.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols
10.2.1.3 – Email Protocols

## Slide 16: Web and Email Protocols SMTP Operation
SMTP is used to send email
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols
10.2.1.4 – SMTP Operation

## Slide 17: Web and Email Protocols POP Operation
POP is used to retrieve email from a mail server.
Email is downloaded from the server to the client and then deleted on the server.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols
10.2.1.5– POP Operation

## Slide 18: Web and Email Protocols IMAP Operation
IMAP is used to retrieve mail from a mail server.
Copies of messages are downloaded from the server to the client and the original messages are stored on the server.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols
10.2.1.6 – IMAP Operation

## Slide 19: Web and Email Protocols Packet Tracer – Web and Email
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.1 – Web and Email Protocols
10.2.1.7 – Packet Tracer – Web and Email

## Slide 20: IP Addressing Services Domain Name Service
Domain names convert the numeric address into a simple, recognizable name.
The DNS protocol defines an automated service that matches resource names with the required numeric network address.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services
10.2.2.1 – Domain Name Service

## Slide 21: IP Addressing Services DNS Message Format
When a client makes a query, the server’s DNS process first looks at its own records to resolve the name.
If unable to resolve, it contacts other servers to resolve the name.
The server temporarily stores the numbered address in the event that the same name is requested again.
The ipconfig /displaydns command displays all of the cached DNS entries on a Windows PC.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services
10.2.2.2 – DNS Message Format

## Slide 22: IP Addressing Services DNS Hierarchy
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services
10.2.2.3 – DNS Hierarchy

## Slide 23: IP Addressing Services The nslookup Command
Nslookup - a utility that allows a user to manually query the name servers to resolve a given host.
  Can also be used to troubleshoot name resolution issues and to verify the current status of the name servers.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services
10.2.2.4 – The nslookup Command

## Slide 24: IP Addressing Services Dynamic Host Configuration Protocol
The Dynamic Host Configuration Protocol (DHCP) for IPv4 automates the assignment of IPv4 addresses, subnet masks, gateways, and other parameters.
DHCP-distributed addresses are leased for a set period of time, then returned to pool for reuse.
DHCP is usually employed for end user devices. Static addressing is used for network devices, such as gateways, switches, servers, and printers.
DHCPv6 (DHCP for IPv6) provides similar services for IPv6 clients.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services
10.2.2.5 – Dynamic Host Configuration Protocol

## Slide 25: IP Addressing Services DHCP Operation
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services
10.2.2.6 – DHCP Operation

## Slide 26: IP Addressing Services Packet Tracer – DHCP and DNS Servers
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services
10.2.2.7 – Packet Tracer – DHCP and DNS Servers

## Slide 27: IP Addressing Services Lab – Observing DNS Resolution
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.2 – IP Addressing Services
10.2.2.8 – Lab – Observing DNS Resolution

## Slide 28: File Sharing Services File Transfer Protocol
FTP requires two connections between the client and the server, one for commands and replies, the other for the actual file transfer:
  The client establishes the first connection to the server for control traffic using TCP port 21.
  The client establishes the second connection to the server for the actual data transfer using TCP port 20.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.3 – File Sharing Services
10.2.3.1 – File Transfer Protocol

## Slide 29: File Sharing Services Server Message Block
The Server Message Block (SMB) is a client/server file sharing protocol:
  SMB file-sharing and print services have become the mainstay of Microsoft networking.
  Clients establish a long-term connection to servers and can access the resources on the server as if the resource is local to the client host.
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.3 – File Sharing Services
10.2.3.2 – Server Message Block

## Slide 30: File Sharing Services Packet Tracer - FTP
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.3 – File Sharing Services
10.2.3.3 – Packet Tracer - FTP

## Slide 31: File Sharing Services Lab – Exploring FTP
Notes: 10.2 – Well-Known Application Layer Protocols and Services
10.2.3 – File Sharing Services
10.2.3.4 – Lab – Exploring FTP

## Slide 32: 10.3 Summary
Notes: 10 – Application Layer
10.3 Summary

## Slide 33: Conclusion Packet Tracer - Explore a Network
Notes: 10.3 – Summary
10.3.1 – Conclusion
10.3.1.2 – Packet Tracer - Explore a Network

## Slide 34: Conclusion Packet Tracer - Multiuser - Tutorial
Notes: 10.3 – Summary
10.3.1 – Conclusion
10.3.1.3 – Packet Tracer - Multiuser - Tutorial

## Slide 35: Conclusion Packet Tracer Multiuser - Implement Services
Notes: 10.3 – Summary
10.3.1 – Conclusion
10.3.1.4 – Packet Tracer Multiuser - Implement Services

## Slide 36: Conclusion Chapter 10: Application Layer
Explain the operation of the application layer in providing support to end-user applications.
Explain how well-known TCP/IP application layer protocols operate.
Notes: 10.3 – Summary
10.3.1 – Conclusion
10.3.1.4 – Chapter 10: Application Layer

## Slide 37: Chapter 10 New Terms and Commands
Bootstrap Protocol (BOOTP)
Simple Mail Transfer Protocol (SMTP)
Post Office Protocol (POP)
Internet Message Access Protocol (IMAP)
File Transfer Protocol (FTP)
Trivial File Transfer Protocol (TFTP)
client-server
Server Message Block (SMB)
Notes: New Terms and Commands